| Key | Property | Description |
| --- | --- | --- |
| 42 | SG1 | Raw strain gage A/D value (0-4095) |
| 43 | SG2 | Raw strain gage A/D value (0-4095) |
| 44 | SG3 | Raw strain gage A/D value (0-4095) |
| 45 | SG4 | Raw strain gage A/D value (0-4095) |
| 46 | SG5 | Raw strain gage A/D value (0-4095) |
| 47 | SG6 | Raw strain gage A/D value (0-4095) |
| 48 | FX | Force in X. Divide by 256 to get Newtons. |
| 49 | FY | Force in Y. Divide by 256 to get Newtons. |
| 50 | FZ | Force in Z. Divide by 256 to get Newtons. |
| 51 | TX | Torque about X. Divide by 4096 to get Newton-meters. |
| 52 | TY | Torque about Y. Divide by 4096 to get Newton-meters. |
| 53 | TZ | Torque about Z. Divide by 4096 to get Newton-meters. |
| 54 | FT | CAN-only. Read returns 2 CAN packets containing all forces and torques. Write (any value) tares the sensor. |
| 55 | AX | Acceleration in X. Divide by 1024 to get m/s^2. |
| 56 | AY | Acceleration in Y. Divide by 1024 to get m/s^2. |
| 57 | AZ | Acceleration in Z. Divide by 1024 to get m/s^2. |
| 58 | GM | Storage area for calibration gain matrix |
| 59 | OV | Storage area for calibration offset vector (unused?) |
| 60 | LED | Debugging variable to set LED states |
| 61 | T1 | Raw thermistor A/D value (0-4095) (location? conversion?) |
| 62 | T2 | Raw thermistor A/D value (0-4095) (location? conversion?) |
| 63 | T3 | Raw thermistor A/D value (0-4095) (location? conversion?) |
| 64 | A | CAN-only. Read returns single CAN packet containing all accelerations. |