P3 JPL Manual

Change History

| Revision | Date | Description | Originator |
| --- | --- | --- | --- |
| AA | 2015-11-13 | Original Issue | B. Zenowich |
| AB | 2016-01-26 | Added some notes for clarification, updated the parameter tables with scaled position info and new homing variables, edited the homing procedure to reflect new method. | B. Zenowich |
| AC | 2016-03-09 | Added information about temperature based parameters and safe position. | C. Woodall |
| AD | 2016-06-28 | Added information on over current and over temperature faults. | C. Woodall |
| AE | 2016-07-27 | Corrected max temperature from 76 °C to 75 °C | C. Woodall |
| AF | 2016-08-31 | Added changes to the document to fit JPL control loop and release. | C. Woodall |
| AG | 2017-01-18 | Exposed raw motor gain parameters | I. Gutekunst |
| AH | 2017-03-03 | Replaced fixed point PI controller with floating point PID controller. Added functionality to plot step responses. Removed homing section. | I. Gutekunst, C. Woodall, B. Zenowich |
| AI | 2017-05-08 | Updated documentation to describe HEARTBEAT parameter. | I. Gutekunst |
| AJ | 2017-06-20 | Updated fraction/units for MV, TENST, and V | I. Gutekunst |

Introduction

P3 is the third-generation of miniature motor controllers (Pucks) from Barrett Technology. In cooperation with NASA JPL, we have integrated P3 directly into the Maxon EC-max 30 (272765) and Maxon EC-max 22 (283860) brushless DC motors. P3 transforms the Maxon motors into bus-topology actuators requiring just 5 wires (Motor+, Logic+, GND, CAN_H, CAN_L) and no separate controllers.

How it works: Cascaded Control Loops

P3 provides an industry-standard motion control architecture. The trajectory generator takes a target position and outputs a series of position commands. The position loop uses angular feedback from the integrated encoder to implement a Proportional-Integral-Derivative (PID) controller which outputs a velocity command. The velocity loop implements a second PID controller which outputs a motor effort. The motor effort is transformed by a space vector function to yield the proper PWM commands to the motor. All of the control inputs are user-adjustable to support application-specific motion control characteristics.

Figure 1: Control Loop Diagram

In Figure 1, the cascaded control loop is represented. Each control loop tuning parameter is represented by its BarrettCAN name. Please see the Motor Control Constants, Example Values for a supported motor(BarrettCAN) Table on page 5 and Page 7 for descriptions of these parameters.

NOTE: We are actively developing the P3 firmware at this time.

How to communicate with it

- We support the Barrett CAN Protocol for full configuration and all modes of operation:

http://web.barrett.com/support/Puck_Documentation/CAN_Message_Format.pdf

- We support a minimal but growing set of CANopen features at this time:

http://web.barrett.com/support/Puck_Documentation/P3_CANopen_revAD.doc

How to control it: Control Modes

There are four distinct control modes that you can choose by setting the MODE property of P3:

- MODE = 0: Idle. The controller ties the motor phase leads together for a resistive-braking effect. No current can flow through the motor.

- MODE = 3: Position control. Write to the P property to set the commanded position.

- MODE = 4: Velocity control. Write to the V property to set the commanded velocity. The motion will obey the acceleration (ACCEL) and max velocity (MV) properties.

- MODE = 5: Trapezoidal velocity profile control. Write to the P property to set the target position. The controller will generate a trapezoidal velocity profile using ACCEL and MV and begin to output a series of commanded positions to the position controller.

About P3 Angular Velocity

You are free to set Max Velocity (MV) to any value you want to achieve your desired motion profile, but take care not to exceed the datasheet’s specifications. For example, the max velocity of the  Maxon EC-Max 22 is 18000 rpm, but the allowable continuous velocity depends on the torque applied to the motor. Please reference the motor datasheets to set these values properly. The controller will obey MV in Position and Velocity modes.

How to update it: In-System Firmware Updates

Methods for updating firmware are included in Barrett’s wxPuck and wxPuckTester applications.

Motor Control Variables (Barrett CAN Protocol)

| Property | Key | Frac | Units | Notes |
| --- | --- | --- | --- | --- |
| T | 42 | 0 | TBD | Open-loop motor effort (read-only) |
| VERS | 0 | 0 | - | Firmware version |
| SN | 2 | 0 | - | Puck serial number |
| ID | 3 | 0 | - | CAN ID |
| ERROR | 4 | 0 | - | Fault status |
| MODE | 8 | 0 | - | Control mode: 0=idle, 3=position, 4=vel, 5=vel profile |
| V | 44 | 4 | rad/s | Gearhead output velocity in Q12.4 (write=cmd, read=actual) |
| P | 48 | 0 | Encoder cts | Motor position (write=cmd, read=actual). Write in MODE=0 to initialize the position value. |
| MOFST | 61 | 0 | Encoder cts | Raw encoder reading at the start of an electrical cycle |
| IOFST | 62 | 0 | A/D cts | Raw A/D reading of current when MODE = 0 |
| MECH | 66 | 0 | Encoder cts | Raw encoder reading (0-4095) |
| CTS | 68 | 0 | Encoder cts | Motor encoder resolution (4096, typ) |
| IKCOR | 93 | 0 | TBD | Motor effort to apply during MOFST calibration |
| TENST | 83 | 4 | Gear Head Ratio * 16 | Gear Head Ratio in Q12.4 units. For example, a gearhead ratio of 300 has TENST = 300*2^4= 4800 |

NOTE: All properties listed here are 16-bits wide, except P which is 32-bits wide.

NOTE: Key = Property key value used in the Barrett CAN Protocol message frames, as described in the CAN_Message_Format.pdf document linked above.

NOTE: Frac = Number of bits of fraction defined for each property. For example, property V (velocity) is a 16-bit integer, but the lower 8 bits are interpreted as a fractional value. So an integer value of 64 for V would be interpreted as 64 / 2^8 = 0.25 rad/s.

Motor Control Constants, Example Values for a supported motor(BarrettCAN)

| Property | Key | Frac | Units | Value | Conv | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| R | 109 | 12 | Ω (/φ) | 0.82 | 3359 | Per-phase or terminal res/2 |
| L | 110 | 12 | mH (/φ) | 0.27 | 1106 | Per-phase or terminal ind/2 |
| J | 111 | 15 | mNms2 | 0.7301 | 23924 | Rotor + gearhead inertia at output |
| KT | 112 | 12 | Nm/ARMS (/φ) | 1.1/3 | 1502 | Per-phase torque constant |
| ICONT | 113 | 0 | TBD | 0.76 ARMS | 800 | Continuous allowed current |
| IPEAK | 114 | 0 | TBD | 1.7 ARMS | 1790 | Peak allowed current |
| IPKMS | 115 | 0 | ms | 1000 | 1000 | Time (in ms) that the current is allowed to exceed ICONT |
| POLES | 90 | 0 | - | 8 | 8 | Rotor magnet count or pole pairs/2 |
| MV | 45 | 4 | rad/s | 100 RPM | 2681 | Max velocity at gearhead output (RPM*2pi/60*256) in Q12.4 |
| VBUS | 21 | 0 | Volts | 24 | 24 | Motor bus voltage |
| MT | 43 | 0 | TBD | 3.5 ARMS | 3685 | ARMS * √2 * 8192/11 The Maximum Torque |
| ACCEL | 82 | 0 | rad/s/(150 us) | 10 | 10 | Used to limit acceleration and deceleration in the velocity and trapezoidal control modes. |

NOTE: All properties listed here are 16-bits wide. The current-related properties never exceed 14-bits in practice.

NOTE: Value is an example value for the property. Conv is that example value converted to the fractional fixed-point value used by the controller.

NOTE: For direct PID control see page 7.

Additional Properties

Errors and Faults

Under the current system there are 2 faults:

- Over-Temperature Faults

- Over-Current Faults

These two faults are handled in different ways and have different parameters associated with them.

Over-Current Faults

The overcurrent faults are run on the commanded currents with a low pass filter, with a cutoff of 20Hz. The commanded current is allowed to run from –IPEAK to IPEAK, currents cannot be commanded which are above IPEAK. If the absolute value of the commanded current, I, is greater than ICONT (the continuous current) a counter starts to increment. If I drops below ICONT the timer restarts. Once the counter has been counting for IPKMS ms the currents are thresholded now to ICONT. If the current I drops below ICONT the limit is released and IPKMS must be exceeded again in order to trigger the overcurrent.

The CANOpen error register flag for current is only held while I is being thresholded to ICONT and is not a permanent state.

Over-Temperature Faults

The over temperature fault is controlled by the following parameters: PTEMP, OTEMP and THERM. PTEMP is the peak temperature, OTEMP is a register which stores the error state, and THERM is the current filtered temperature. The THERM temperatures are filtered with a 20Hz cutoff and are mapped from the raw values to temperature using a multiple region linear interpolation which has a max error of 1 °C in the main operational zones and can peak to 2 °C at temperatures below 20 °C.

The over-temperature fault is triggered when THERM is greater than PTEMP for more than 5 seconds (hard-coded). PTEMP is not allowed to be greater than 75 °C. When the over-temperature fault is generated OTEMP will read back 1. If you write any value to OTEMP it will clear the error. When the fault occurs motor currents are forced to 0.

The CANOpen error register flag is set the whole time the ERROR flag is set until it is cleared, which can only be cleared in CANOpen through a reset.

Heartbeat Timeout Fault

If HEARTBEAT is nonzero, and the puck doesn’t receive a successful can communication (read or write) for HEARTBEAT ms, it will transition to IDLE. If HEARTBEAT is set to 0, the timeout won’t occur. To clear the fault, simply write to MODE to start the motor again.

Direct Control of PID Control Parameters

The raw values used by the velocity and position PID controllers have been exposed in the latest firmware revision.

Due to implementation details, the parameters are exposed as a Q8.8 gain with a multiplication factor (Mult).

For example, Actual KP = property[KP] * 10

Raw Controller Inputs

| Property | Key | Frac | Mult | Notes |
| --- | --- | --- | --- | --- |
| KP | 79 | 8 | 10 | Position KP |
| KI | 80 | 8 | 1 | Position KI |
| KD | 81 | 8 | 1 | Position KD |
| VKP | 119 | 8 | 10 | Velocity KP |
| VKI | 120 | 8 | 1 | Velocity KI |
| VKD | 124 | 8 | 1 | Velocity KD |
| VKFF | 126 | 8 | 1 | Velocity feed forward gain |

Plotting Step Responses

The wxPuck Tester Utility has facilities for plotting step responses.

- Set desired gains

- Click “Do V Step Response”, or “Do P Step Response”.

- After the motor has finished moving (< 2 seconds), click Plot or Save CSV It will take about 30 seconds to download the trace data. During this time, the GUI and motor will not respond to any input.

- Save the plots from the plot window.

Notes: The position step response will move the motor by 4096 encoder ticks. The velocity step response will set a velocity of 50 rad/s  at the output shaft. The motor will attempt to reach TENST * 50 rad/s

# Text boxes

| Property | Key | Frac | Units | Value | Conv | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| THERM | 20 | 8 | °C | 40 °C | 10240 | Thermistor temperature in °C (16-bit number in Q8.8 format. Temperature * 2^8) |
| PTEMP | 10 | 8 | °C | 70 °C | 17920 | Peak temperature in °C (16-bit number in Q8.8 format. Temperature * 2^8) |
| OTEMP | 11 | 0 | Bool | 1 | Fault | Temperature Fault and Fault Reset property. |
| HEARTBEAT | 123 | 0 | ms | 0 | None | Heartbeat expiration delay in ms. Set to 0 to disable. |