P3/RSF-5B Manual

Change History

| Revision | Date | Description | Originator |
| --- | --- | --- | --- |
| AA | 2015-11-13 | Original Issue | B. Zenowich |
| AB | 2016-01-26 | Added some notes for clarification, updated the parameter tables with scaled position info and new homing variables, edited the homing procedure to reflect new method. | B. Zenowich |
| AC | 2016-03-09 | Added information about temperature based parameters and safe position. | C. Woodall |
| AD | 2016-06-28 | Added information on over current and over temperature faults. | C. Woodall |
| AE | 2016-07-27 | Corrected max temperature type from 76 to 75 deg C | C. Woodall |
| AF | 2017-07-19 | Documented all BarrettCAN parameters used in the GUI. | B. Zenowich |

Introduction

P3 is the third-generation of miniature motor controllers (Pucks) from Barrett Technology. In cooperation with Harmonic Drive, we have integrated P3 directly into an RSF-5B actuator which consists of a brushless DC motor with a compact gearhead. P3 transforms the RSF-5B from a star-topology actuator requiring at least 9 home-run wires between each actuator and its corresponding controller (A, B, C, U, V, W, 5V, Motor+, GND) to a bus-topology actuator requiring just 4 wires (Motor+, GND, CAN_H, CAN_L) and no separate controllers.

How it works: Cascaded Control Loops

P3 provides an industry-standard motion control architecture. The trajectory generator takes a target position and outputs a series of position commands. The position loop uses angular feedback from the integrated encoder to implement a Proportional-Integral (PI) controller which outputs a velocity command. The velocity loop implements a second PI controller which outputs a current command. The current loop uses current sensor feedback to implement a third PI controller whose output is sent to a space-vector function to yield the proper PWM command to the motor. Each of the controllers has an adjustable bandwidth you can use to fine-tune the motion control characteristics.

Figure 1: Control Loop Diagram

Note: We are actively developing the P3 firmware at this time. We have not yet completed the velocity loop filters as of 2017-07-19.

How to communicate with it

- We support the Barrett CAN Protocol for full configuration and all modes of operation:

http://web.barrett.com/support/Puck_Documentation/CAN_Message_Format.pdf

- We support a minimal but growing set of CANopen features at this time:

http://web.barrett.com/support/Puck_Documentation/P3_CANopen.doc

- We plan to support Modbus RTU (multi-drop RS-485) in a future firmware release.

How to control it: Control Modes

There are five distinct control modes that you can choose by setting the MODE property of P3:

- MODE = 0: Idle. The controller ties the motor phase leads together for a resistive-braking effect. No current can flow through the motor.

- MODE = 2: Current control. Write to the T property to set the motor current directly. Note that the Max Velocity (MV) property is ignored in this mode, so you must be careful to watch the velocity (V) yourself and reduce T if necessary.

- MODE = 3: Position control. Write to the P property to set the commanded position.

- MODE = 4: Velocity control. Write to the V property to set the commanded velocity.

- MODE = 5: Trapezoidal velocity profile control. Write to the P property to set the target position. The controller will generate a trapezoidal velocity profile using ACCEL and MV and begin to output a series of commanded positions to the position controller. (NOTE: This mode is still under development).

About P3 Motor Currents

Motor currents are always 14-bits wide (-8192..8191) corresponding to (-11..11) APK. Divide APK by √2 to get ARMS. Commanded motor current is limited to the lower of IPEAK or MT. If the average motor current is above ICONT for more than IPKMS milliseconds, the commanded current will fall back to ICONT until the commanded motor current drops below ICONT.

About P3 Angular Velocity

Unlike current, there is no absolute limit for velocity, and the controller does not differentiate between continuous or peak velocities. You are free to set Max Velocity (MV) to any value you want to achieve your desired motion profile, but take care not to exceed the datasheet’s specifications. For example, the max velocity of the RSF-5B-100 is 100 RPM, but the allowable continuous velocity is 45 RPM. The controller will obey MV in Position and Velocity modes, not Torque mode.

How to update it: In-System Firmware Updates

We provide a Windows-based firmware updater here:

http://web.barrett.com/support/Puck_Firmware/P3_Update.zip

Follow the directions in that folder’s README.txt file to update the P3 firmware over CAN.

Motor Control Variables (Barrett CAN Protocol)

| Property | Key | Frac | Units | Notes |
| --- | --- | --- | --- | --- |
| T | 42 | 0 | APK*8192/11 | Motor current command |
| VERS | 0 | 0 | - | Firmware version |
| SN | 2 | 0 | - | Puck serial number |
| ID | 3 | 0 | - | CAN ID |
| ERROR | 4 | 0 | - | Fault status |
| MODE | 8 | 0 | - | Control mode: 0=idle, 2=torque, 3=position, 4=vel |
| V | 44 | 8 | rad/s | Gearhead output velocity (write=cmd, read=actual) |
| P | 48 | 0 | Encoder cts | Motor position (write=cmd, read=actual) |
| MOFST | 61 | 0 | Encoder cts | Raw encoder reading at the start of an electrical cycle |
| IOFST | 62 | 0 | A/D cts | Raw A/D reading of current when MODE = 0 |
| MECH | 66 | 0 | Encoder cts | Raw encoder reading (0-4095) |
| CTS | 68 | 0 | Encoder cts | Motor encoder resolution (4096, typ) |
| IKCOR | 93 | 0 | APK*8192/11 | Current to apply during MOFST calibration |
| SCLCMD | 63 | 0 |  | 16-bit command position, scaled between the two soft-stops |
| SCLFBK | 64 | 0 |  | 16-bit position feedback, scaled between the two soft-stops |
| IMOTOR | 22 | 0 | APK*8192/11 | Motor current feedback |
| STAT | 5 | 0 | - | Status: 2 = Ready, 3 = Homing |

NOTE: All properties listed here are 16-bits wide.

NOTE: Key = Property key value used in the Barrett CAN Protocol message frames, as described in the CAN_Message_Format.pdf document linked above.

NOTE: Frac = Number of bits of fraction defined for each property. For example, property V (velocity) is a 16-bit integer, but the lower 8 bits are interpreted as a fractional value. So an integer value of 64 for V would be interpreted as 64 / 2^8 = 0.25 rad/s.

Motor Control Constants, Example Values for RSF-5B-100 (Barrett CAN Protocol)

| Property | Key | Frac | Units | Value | Conv | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| R | 109 | 12 | Ω (/φ) | 0.82 | 3359 | Per-phase or terminal res/2 |
| L | 110 | 12 | mH (/φ) | 0.27 | 1106 | Per-phase or terminal ind/2 |
| J | 111 | 15 | mNms2 | 0.7301 | 23924 | Rotor + gearhead inertia at output |
| KT | 112 | 12 | Nm/ARMS (/φ) | 1.1/3 | 1502 | Per-phase torque constant |
| ICONT | 113 | 0 | APK*8192/11 | 0.76 ARMS | 800 | ARMS * √2 * 8192/11 |
| IPEAK | 114 | 0 | APK*8192/11 | 1.7 ARMS | 1790 | ARMS * √2 * 8192/11 |
| IPKMS | 115 | 0 | ms | 1000 | 1000 | See NOTE 2, above |
| IBW | 116 | 0 | Hz | 300 | 300 | Current control bandwidth R/(2pi * L), typ |
| VBW | 117 | 0 | Hz | 25 | 25 | Velocity control bandwidth, IBW/10, typ |
| PBW | 118 | 8 | Hz | 0.94 | 240 | Position control bandwidth, VBW/10, typ |
| POLES | 90 | 0 | - | 8 | 8 | Rotor magnet count or pole pairs/2 |
| MV | 45 | 8 | rad/s | 100 RPM | 2681 | Max velocity at gearhead output (RPM*2pi/60*256) |
| VBUS | 21 | 0 | Volts | 24 | 24 | Motor bus voltage (nominal) |
| VSENSE | 23 | 8 | Volts | 24 | 6144 | Motor bus voltage (sensed) |
| MT | 43 | 0 | APK*8192/11 | 3.5 ARMS | 3685 | ARMS * √2 * 8192/11 |
| ACCEL | 82 | 0 | rad/s/150 uS | 10 | 10 | Only used in position control |
| RATIO | 83 | 8 | - | 100 | 25600 | Gear ratio |
| FILT_Q | 14 | 8 |  | 0.7071 | 181 | Smoothing filter Q value. Use 0.7071 for Butterworth filter. |
| FILT_FC | 15 | 15 | Hz * 6.67e3 | 28.892 | 142 | Smoothing filter cutoff frequency |
| FILT_EN | 16 | 0 | Bool | 0 | False | Enable smoothing filter |
| MACH | 1 | 0 | - | 0 | 0 | User-settable machine code |
| ROLE | 105 | 0 | - | 0 | 0 | User-settable role code |

NOTE: All properties listed here are 16-bits wide. The current-related properties never exceed 14-bits in practice.

Homing Constants (Barrett CAN Protocol)

| Property | Key | Frac | Units | Value | Conv | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| MDS | 65 | 0 | ms | 1000 | 1000 | Auto-home delay, 0 = No auto-homing |
| IVEL | 73 | 8 | rad/s | 10 RPM | 268 | Initialization velocity, + = CW homing, - = CCW homing |
| IHIT | 108 | 0 | APK*8192/11 | 0.19 ARMS | 200 | Homing current threshold |
| IOFF | 74 | 0 | Encoder cts | 20000 | 20000 | CW hard-stop offset |
| JOFST | 98 | 0 | Encoder cts | 40000 | 40000 | CCW hard-stop offset |
| DP | 50 | 0 | 16-bit scaled | 32768 | 32768 | Default position after homing (0-65535) |
| E | 52 | 0 | Encoder cts | 0 | 0 | Single-ended homing offset |
| DS | 60 | 8 | rad/s | 20 RPM | 536 | Post-homing move velocity |

NOTE: Properties with units of “Encoder cts” are 32-bits wide. All others are 16-bits wide.

Homing Procedure

If MDS > 0, auto-homing will begin MDS milliseconds after the motor control firmware begins executing. If MDS = 0, auto-homing is disabled. Set CMD(29) to CMD_HI(13) to initiate homing (or to re-home).

The sign of IVEL determines the initial direction of movement during homing. Dual hard-stop homing requires non-zero values for both IOFF and JOFST (the CW and CCW hard-stop offsets) and E must be set to zero. If you want CW single hard-stop homing, set IOFF, E, and IVEL to positive values. If you want CCW single hard-stop homing, set JOFST and E to positive values and set IVEL to a negative value.

Before starting, the max motor torque is limited to IHIT. The motor then starts moving with a velocity of IVEL until the sensed velocity becomes zero AND the motor current saturates at IHIT. Then the motor reverses direction by setting its velocity to –IVEL.

If this is single-ended homing, then the motor runs until the proper number of encoder counts has passed (IOFF or JOFST, depending on which stop it just hit). The controller then initializes its position value with either 0 or E, depending on the homing direction. Then it moves to its default starting position (DP) using the post-homing move velocity (DS).

If this is double-ended homing, then the motor runs until it hits the second hard-stop (sensed velocity becomes zero AND the motor current saturates at IHIT). Then the motor reverses direction again by restoring its velocity to IVEL. It runs until the proper number of encoder counts has passed (IOFF or JOFST, depending on which stop it just hit). Then it moves to its default starting position (DP) using the post-homing move velocity (DS).

The controller is left in position-control mode after homing so that it is ready to accept a stream of commanded positions.

NOTE: The controller does not verify the operational range during double-ended homing.

NOTE: IOFF and/or JOFST should contain positive values corresponding to the number of encoder counts to traverse after hitting a hard-stop. IOFF = number of encoder counts to back off from the CW stop before setting its CW soft-stop there. JOFST = number of encoder counts to back off from the CCW stop before setting its CCW soft-stop there.

NOTE: Soft-stops are disabled until the homing routine completes.

Additional Properties

| Property | Key | Frac | Units | Value | Conv | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| THERM | 20 | 8 | Deg C | 40 deg C | 10240 | Thermistor temperature in degrees C (16-bit number in Q8.8 format. Temperature * 2^8) |
| PTEMP | 10 | 8 | Deg C | 70 deg C | 17920 | Peak temperature in degrees C (16-bit number in Q8.8 format. Temperature * 2^8) |
| OTEMP | 11 | 0 | Bool | 1 | Fault | Temperature Fault and Fault Reset property. |
| TACT | 106 | 0 | 16-bit scaled positions | 32768 | 32768 | Safe Position (16-bit scaled positions 0 to 65535) |
| TERM | 34 | 0 | Bool | 1 | True | Enable CAN termination |

Errors and Faults

There are two faults when using BarrettCAN:

- Over-Temperature Faults

- Over-Current Faults

Over-Current Faults

The overcurrent faults are run on the commanded currents with a low pass filter, with a cutoff of 20Hz. The commanded current is allowed to run from –IPEAK to IPEAK, currents cannot be commanded which are above IPEAK. If the absolute value of the commanded current, I, is greater than ICONT (the continuous current) a counter starts to increment. If I drops below ICONT the timer restarts. Once the counter has been counting for IPKMS ms the currents are thresholded now to ICONT. If the current I drops below ICONT the limit is released and IPKMS must be exceeded again in order to trigger the overcurrent.

The CANOpen error register flag for current is only held while I is being thresholded to ICONT and is not a permanent state.

Over-Temperature Faults

The over temperature fault is controlled by the following parameters: PTEMP, OTEMP and THERM. PTEMP is the peak temperature, OTEMP is a register which stores the error state, and THERM is the current filtered temperature. The THERM temperatures are filtered with a 20Hz cutoff and are mapped from the raw values to temperature using a multiple region linear interpolation which has a max error of 1 deg. C in the main operational zones and can peak to 2 degrees C at temperatures below 20 degrees C.

The over-temperature fault is triggered when THERM is greater than PTEMP for more than 5 seconds (hard-coded). PTEMP is not allowed to be greater than 75 degrees C. When the over-temperature fault is generated OTEMP will read back 1. If you write any value to OTEMP it will clear the error. When the fault occurs motor currents are forced to 0.

The CANOpen error register flag is set the whole time the ERROR flag is set until it is cleared, which can only be cleared in CANOpen through a reset.