Puck commands (property 29)

Usage:

SET CMD <VALUE>

SET 29 <some command from the list below>

| Key | Command | Description |
| --- | --- | --- |
| 0 | cmdLoad | Load a property from EEPROM (if value = -1, load all properties) |
| 1 | cmdSave | Save a property to EEPROM (if value = -1, save all properties) |
| 2 | cmdReset | Reset the puck firmware (soft reboot) |
| 3 | cmdDef | Set a property to its default. Deprecated. Use btutil, instead. |
| 4 | cmdGet | Used internally. Do not use. |
| 5 | cmdFind | Used internally. Use SET FIND(33) MOFST(61) instead, for example. |
| 6 | cmdSet | Used internally. Do not use. |
| 7 | cmdHome | Go to the home position (zero) |
| 8 | cmdKeep | Keep and process received serial characters (default state) |
| 9 | cmdLoop | Start the serial realtime control loop. Not yet implemented. |
| 10 | cmdPass | Pass serial characters through to secondary serial port (for testing) |
| 11 | cmdVers | Used internally. Use GET VERS(0) instead. |
| 12 | cmdErr | Used internally. Do not use. |
| 13 | cmdHI | Perform Hand-Initialization routine for this motor |
| 14 | cmdIC | Incremental Close (moves motor by +Default Step DS encoder counts) |
| 15 | cmdIO | Incremental Open (moves motor by –Default Step DS encoder counts) |
| 16 | cmdTC | Torque Close (closes with MT, not velocity limited) |
| 17 | cmdTO | Torque Open (opens with MT, not velocity limited) |
| 18 | cmdClose | Close, move to encoder position specified by Close Target (CT) |
| 19 | cmdMove | Move to encoder position specified by Default Position (DP) |
| 20 | cmdOpen | Open, move to encoder position specified by Open Target (OT) |
| 21 | cmdTerm | Terminate motor power. Equivalent to SET MODE 0. |
| 22 | cmdHelp | Not yet implemented |
| 23 | cmdPPSInit | Used internally. Do not use. |
| 24 | cmdTestEE | Test the EEPROM with alternating bit-patterns. Sets ERROR. |