P3 CANopen Manual

Change History

| Revision | Date | Description | Originator |
| --- | --- | --- | --- |
| AA | 2016-01-18 | Original Issue | B. Zenowich |
| AB | 2016-01-18 | Fixed Scaled Feedback OD Index | B. Zenowich |
| AC | 2016-01-19 | Added more detail to Example Operation, added change history. | B. Zenowich |
| AD | 2016-01-19 | Restored change history after accidental deletion. | B. Zenowich |
| AE | 2016-02-10 | Added documentation for the “set mode” entry in the OD (index = 0x6060). | C. Woodall |
| AF | 2016-02-24 | Added documentation for the “Error” entry in the OD (index = 0x1001) Added example of how to check for an over-temperature fault. | C. Woodall |
| AG | 2016-03-01 | Added information on CANOpen OD entry 0x3F00 for accessing BarrettCAN properties Added examples for using property 0x3F00 | C. Woodall |
| AH | 2016-04-13 | Added Appendix B on supporting multi-field TPDOs | C. Woodall |
| AI | 2016-04-22 | Added safe position information. | C. Woodall |

Supports:

- Network Management (NMT) messages

- Heartbeat producer

- Expedited Service Data Object (SDO) messages

- Byte-level Receive/Transmit Process Data Objects (RPDOs/TPDOs)

- Sync messages for RPDOs/TPDOs

- Up to 4 RPDOs and 4 TPDOs

- Up to 4 mappable objects per PDO

- Dynamic RPDO/TPDO configuration

- SDO abort message generation

- Optional “Boot to Operational State”

- Single pair of static SDO Connection Object Identifiers (COB IDs), 0x600/0x580 + NodeID

- 11-bit CAN 2.0A identifiers

Does not yet support:

- Emergency messages

- Heartbeat consumption

- Timestamps

- Segmented SDOs

- Block transfer SDOs

- SDO size indication (all Tx SDOs are 8 bytes regardless of payload type)

- Bit-level RPDOs/TPDOs

- Remote Transmit Request (RTR) messages

- Multiple/dynamic SDO COB IDs

- NMT master discovery

- TPDO inhibit timers

- TPDO event timers

- 29-bit CAN 2.0B identifiers

- Object Dictionary “dummy” entries

Boot Sequence

- Initialize DSP

- Wait for NMT state message (typ. Pre-op or Operational)

- Initialize CANopen subsystem

- Transmit heartbeat message

- Enter specified state

States

- Boot-up

  - Does not consume any messages

  - Only able to produce the boot-up message

  - Automatically enters Pre-op state after initialization and boot-up transmission

- Stopped

  - Communication limited to NMT and heartbeats only

- Pre-operational

  - All messages except PDOs are allowed

  - Note: How should we respond to SYNC messages in this state?

- Operational

  - All messages are allowed

- Reset Node

  - Performs a power-on reset (full reset)

- Reset Communication

  - Resets the CAN device then enters Boot-up state

Object Dictionary:

| Term | Definition |
| --- | --- |
| U08 | Unsigned 8-bit integer |
| U16 | Unsigned 16-bit integer |
| U32 | Unsigned 32-bit integer |
| RO | Read-Only |
| RW | Read-Write |

| Index | SubIdx | Type | Access | Description |
| --- | --- | --- | --- | --- |
| 0x1000 | 0 | U32 | RO | Device Type low16=profile, high16=addt'l info |
| 0x1001 | 0 | U08 | RO | Error (Bit 0 = Generic, Bit 3 = Temperature) |
| 0x1005 | 0 | U32 | RW | Sync COB ID |
| 0x1006 | 0 | U32 | RO | Sync period in microseconds (iff producer) |
| 0x1008 | 0 | STR | RO | Mfg device name (4 chars) |
| 0x1009 | 0 | STR | RO | Mfg hardware version (4 chars) |
| 0x1010 | 0 | U08 | RO | Save, number of entries = 1 |
| 0x1010 | 1 | U32 | RW | Save All (write 0x65766173 “SAVE”) |
| 0x100A | 0 | STR | RO | Mfg software version (4 chars) |
| 0x1014 | 0 | U32 | RW | Emergency COB ID (default = 0x80 + NodeID) |
| 0x1015 | 0 | U16 | RW | Emergency inhibit time |
| 0x1017 | 0 | U16 | RW | Heartbeat period in milliseconds |
| 0x1018 | 0 | U08 | RO | Identity, number of entries = 6 |
| 0x1018 | 1 | U32 | RW | Vendor ID |
| 0x1018 | 2 | U32 | RW | Product code |
| 0x1018 | 3 | U32 | RW | Revision number |
| 0x1018 | 4 | U32 | RW | Serial number |
| 0x1018 | 5 | U32 | RW | Machine code |
| 0x1018 | 6 | U32 | RW | Role code |
| 0x1200 | 0 | U08 | RO | SDO parameters, number of entries = 2 |
| 0x1200 | 1 | U32 | RO | SDO receive COB ID, default = 0x600 + NodeID |
| 0x1200 | 2 | U32 | RO | SDO transmit COB ID, default = 0x580 + NodeID |
| 0x1400-0x1403 | 0 | U08 | RO | RPDO parameters, number of entries = 2 |
| 0x1400-0x1403 | 1 | U32 | RW | RPDO COB ID |
| 0x1400-0x1403 | 2 | U08 | RW | RPDO Rx type: 0-240 = Apply on nth Sync, 254 = Mfg specific, 255 = Async (Apply upon receipt) |
| 0x1600-0x1603 | 0 | U08 | RW | RPDO mapping, number of mapped objects (0-4) |
| 0x1600-0x1603 | 1-4 | U32 | RW | RPDO mapping, bits 16-31: Index, bits 8-15: SubIdx, bits 0-7 bit length (8, 16, or 32 bits) |
| 0x1800-0x1803 | 0 | U08 | RO | TPDO parameters, number of entries = 5 |
| 0x1800-0x1803 | 1 | U32 | RW | TPDO COB ID |
| 0x1800-0x1803 | 2 | U08 | RW | TPDO Tx type: 0-240 = Tx on nth Sync, 254 = Mfg specific, 255 = Async |
| 0x1800-0x1803 | 3 | U16 | RW | TPDO inhibit time in multiples of 100 uS (not implemented) |
| 0x1800-0x1803 | 4 | U08 | RO | Unused |
| 0x1800-0x1803 | 5 | U16 | RW | TPDO event timer in ms |
| 0x1A00-0x1A03 | 0 | U08 | RW | TPDO mapping, number of mapped objects (0-4) |
| 0x1A00-0x1A03 | 1-4 | U32 | RW | TPDO mapping, bits 16-31: Index, bits 8-15: SubIdx, bits 0-7 bit length (8, 16, or 32 bits) |
| 0x2201 | 0 | I16 | RO | Bus voltage returned as a Q8.8 signed integer. |
| 0x2202 | 0 | I16 | RO | Ambient temperature returned as a Q8.8 signed integer. |
| 0x2401 | 0 | U16 | RW | 16-bit Unsigned Scaled Safe Position. |
| 0x3F00 | 0-127 | U32 | RO | BarrettCAN Property Access. The sub-index maps to the BarrettCan Property. So sub-index 20 (0x14) will read the THERM property and sub-index 50 (0x32) will read the DP parameter. |
| 0x6060 | 0 | U32 | RW | Set mode of operation (0 = IDLE, 1 = POSITION, 3 = VELOCITY, 4 = TORQUE, 6 = HOMING) |
| 0x6061 | 0 | U32 | RO | Read mode of operation |
| 0x60A0 | 0 | U16 | RW | Scaled position command |
| 0x60A1 | 0 | U16 | RO | Scaled position feedback |
| 0x1F80 | 0 | U32 | RW | NMT startup (0 = Boot to Operational, 4 = Boot to Pre-op) |

Example configuration for Node 1:

<MessageID> [Data Length Code] byte0 byte1… (all in hexadecimal)

# Go Pre-op (switches from BarrettCAN to CANopen,

# PDOs not processed in Pre-op)

<0x000> [2] 80 01 (NMT)

<0x701> [1] 7f (heartbeat)

# Set Sync COB ID to 0x080

<0x601> [8] 22 05 10 00 80 00 00 00 (set)

<0x581> [8] 60 05 10 00 80 00 00 00 (ack)

# Set Heartbeat MS to 0x03E8 = 1000 ms

<0x601> [6] 22 17 10 00 E8 03 (set)

<0x581> [8] 60 17 10 00 E8 03 00 00 (ack)

# Set RPDO_1 COB ID (0x1400,1) to 0x201

<0x601> [8] 22 00 14 01 01 02 00 00 (set)

<0x581> [8] 60 00 14 01 01 02 00 00 (ack)

# Set RPDO_1 Rx type (0x1400,2) to 0xFF (async, process immediately,

# do not wait for SYNC)

<0x601> [5] 22 00 14 02 FF (set)

<0x581> [8] 60 00 14 02 FF 00 00 00 (ack)

# Set RPDO_1 first mapping (0x1600,1) to 0x60A0,0 (Scaled position cmd,

# 16-bits)

<0x601> [8] 22 00 16 01 10 00 A0 60 (set)

<0x581> [8] 60 00 16 01 10 00 A0 60 (ack)

# Set RPDO_1 mapping count (0x1600,0) to 1

<0x601> [5] 22 00 16 00 01 (set)

<0x581> [8] 60 00 16 00 01 00 00 00 (ack)

# Set TPDO_1 COB ID (0x1800,1) to 0x181

<0x601> [8] 22 00 18 01 81 01 00 00 (set)

<0x581> [8] 60 00 18 01 81 01 00 00 (ack)

# Set TPDO_1 Tx type (0x1800,2) to 0 (Tx on every SYNC)

<0x601> [5] 22 00 18 02 00 (set)

<0x581> [8] 60 00 18 02 00 00 00 00 (ack)

# Set TPDO_1 Inhibit time (0x1800,3) to 0 (unused)

<0x601> [6] 22 00 18 03 00 00 (set)

<0x581> [8] 60 00 18 03 00 00 00 00 (ack)

# Set TPDO_1 Event timer (0x1800,5) to 0 (unused)

<0x601> [6] 22 00 18 05 00 00 (set)

<0x581> [8] 60 00 18 05 00 00 00 00 (ack)

# Set TPDO_1 first mapping (0x1A00,1) to 0x60A1,0 (Scaled position feedback,

# 16-bits)

<0x601> [8] 22 00 1A 01 10 00 A1 60 (set)

<0x581> [8] 60 00 1A 01 10 00 A1 60 (ack)

# Set TPDO_1 mapping count (0x1A00,0) to 1

<0x601> [5] 22 00 1A 00 01 (set)

<0x581> [8] 60 00 1A 00 01 00 00 00 (ack)

# Save object dictionary changes to EEPROM (write “SAVE” to 0x1010,1)

<0x601> [8] 22 10 10 01 73 61 76 65 (set)

<0x581> [8] 60 10 10 01 01 00 00 00 (ack, reading this object returns 1 = manual write support)

# Reboot node 1

<0x000> [2] 81 01 (NMT)

Example operation:

# Apply power

# Wait at least 5 ms for P3 to boot up

# Go Operational (switches from BarrettCAN to CANopen, RPDOs and TPDOs enabled)

<0x000> [2] 01 00 	NMT – Go Operational, all nodes

# Initial heartbeats

<0x701> [1] 05 	Puck 1 responds with its initial heartbeat

<0x702> [1] 05 	Puck 2 responds with its initial heartbeat

# First control loop iteration, RPDOs sent from master to pucks

<0x201> [2] 34 12 	Master sends Puck 1 a scaled position command = 0x1234

<0x202> [2] 56 34 	Master sends Puck 2 a scaled position command = 0x3456

# Master asks for puck TPDOs

<0x080> [0] 	Master sends a Sync to get position feedback from all nodes

# Pucks respond with their TPDOs

<0x181> [2] 20 12 	Puck 1 responds with its scaled position feedback = 0x1220

<0x182> [2] 50 34 	Puck 2 responds with its scaled position feedback = 0x3450

# Second control loop iteration…

<0x201> [2] 56 12 	Master sends Puck 1 a scaled position command = 0x1256

<0x202> [2] 89 34 	Master sends Puck 2 a scaled position command = 0x3489

<0x080> [0] 	Master sends a Sync to get position feedback from all nodes

<0x181> [2] 33 12 	Puck 1 responds with its scaled position feedback = 0x1233

<0x182> [2] 85 34 	Puck 2 responds with its scaled position feedback = 0x3485

# … N iterations

Example Retrieving an Error:

# In the GO-OP state

# Check Puck 1s Error Register (0x1001,0)

<0x601> [5] 40 01 10 00 00  (read)

# IF there is a temperature error

# NOTE: To clear this error, a power cycle or reset of the node is necessary.

<0x581> [8] 42 01 10 00 09 00 00 00 # Bit 3 (Temperature) and Bit 0 (Generic) are set (0x8 + 0x1)

# OTHERWISE

<0x581> [8] 42 01 10 00 00 00 00 00 # No bits are set

Example operation, reading BarrettCAN parameters:

# In The GO-OP State

# Get the Default Position (DP) property 50.

<0x601> [4] 40 00 3F 32

<0x581> [8] 42 00 3F 32 00 80 00 00

# Get the Thermistor Temperature (THERM) property 20.

<0x601> [4] 40 00 3F 14

<0x581> [8] 42 00 3F 32 00 1E 00 00

Appendix A – CANopen Message Format

- Network Management (NMT)

  - MsgID = 0x000 (heard by all nodes)

  - DLC = 2

  - Payload = [Commanded_State] [NodeID]

    - Commanded_State

      - 0x01 = Operational

      - 0x02 = Stopped

      - 0x80 = Pre-operational

      - 0x81 = Reset Node

      - 0x82 = Reset Communications

    - NodeID

      - 0 = All nodes

      - >0 = Single node

- Heartbeat

  - MsgID = 0x700 | NodeID

  - DLC = 1

  - Payload = [State]

    - State

      - 0x00 = Boot-up

      - 0x04 = Stopped

      - 0x05 = Operational

      - 0x7F = Pre-operational

- SYNC

  - MsgID = 0x080

  - DLC  = 0

- Emergency

  - MsgID = 0x080 | NodeID

  - DLC = 8

  - Payload = [ErrLow] [ErrHigh] [ErrRegister] [Mfg-Specific]…

    - [ErrLow] [ErrHigh] = 16-bit CANopen error code

    - [ErrRegister] = copy of OD 1001,00

    - [Mfg-Specific] = 0-5 bytes of error data (optional)

- Timestamp

  - MsgID = 0x100

  - DLC = 4

  - Payload = 32-bit timestamp value (LSB)

- SDO Write (Expedited) – Write this data to the Object Dictionary (OD)

  - MsgID = 0x600 | NodeID

  - DLC = 8

  - Payload = [0010 nn e s] [lowIdx] [highIdx] [subIdx] [ data ]…

    - 0010 = SDO Write

    - nn = number of bytes w/o data (iff s == 1)

    - e = Expedited

    - s = size indicated in nn

    - [lowIdx] [highIdx] = 16-bit OD index

    - [subIdx] = OD entry sub-index

    - [data] = 1-4 bytes of data (little-endian)

- SDO Write Ack – Data was written to the OD

  - MsgID = 0x580 | NodeID

  - DLC = 8

  - Payload = [0110 0000] [lowIdx] [highIdx] [subIdx] 0x00 0x00 0x00 0x00

- SDO Read – Read data from OD

  - MsgID = 0x600 | NodeID

  - DLC = 8

  - Payload = [0100 0000] [lowIdx] [highIdx] [subIdx] 0x00 0x00 0x00 0x00

- SDO Read Response (Expedited) – Here is the data you requested

  - MsgID = 0x580 | NodeID

  - DLC = 8

  - Payload = [0100 nn e s] [lowIdx] [highIdx] [subIdx] [ data ]…

    - 0100 = SDO Read

    - nn = number of bytes w/o data (iff s == 1)

    - e = Expedited

    - s = size indicated in nn

    - [lowIdx] [highIdx] = 16-bit OD index

    - [subIdx] = OD entry sub-index

    - [data] = 1-4 bytes of data (little-endian)

- Receive PDO – process data object to be received by the device

  - MsgID = 0x200 | NodeID, 0x300 | NodeID, etc.

  - DLC = n (byte count)

  - Payload = [data]…

    - [data] = little-endian data

- Transmit PDO – process data object to be transmitted by the device

  - MsgID = 0x180 | NodeID, 0x280 | NodeID, etc.

  - DLC = n (byte count)

  - Payload = [data]…

    - [data] = little-endian data

Appendix B – CANopen Multi-Field TPDO

# Set TPDO_1 COB ID (0x1800,1) to 0x181

<0x601> [8] 22 00 18 01 81 01 00 00 (set)

<0x581> [8] 60 00 18 01 81 01 00 00 (ack)

# Set TPDO_1 Tx type (0x1800,2) to 0 (Tx on every SYNC)

<0x601> [5] 22 00 18 02 00 (set)

<0x581> [8] 60 00 18 02 00 00 00 00 (ack)

# Set TPDO_1 Inhibit time (0x1800,3) to 0 (unused)

<0x601> [6] 22 00 18 03 00 00 (set)

<0x581> [8] 60 00 18 03 00 00 00 00 (ack)

# Set TPDO_1 Event timer (0x1800,5) to 0 (unused)

<0x601> [6] 22 00 18 05 00 00 (set)

<0x581> [8] 60 00 18 05 00 00 00 00 (ack)

# Set TPDO_1 first mapping (0x1A00,1) to 0x60A1,0 (Scaled position feedback, 16-bits)

<0x601> [8] 22 00 1A 01 10 00 A1 60 (set)

<0x581> [8] 60 00 1A 01 10 00 A1 60 (ack)

# Set TPDO_1 second mapping (0x1A00,2) to 0x2201,0 (Bus voltage, 16-bits)

<0x601> [8] 22 00 1A 02 10 00 01 22 (set)

<0x581> [8] 60 00 1A 02 10 00 01 22 (ack)

# Set TPDO_1 third mapping (0x1A00,3) to 0x2202,0 (Amplifier temperature, 16-bits)

<0x601> [8] 22 00 1A 03 10 00 02 22 (set)

<0x581> [8] 60 00 1A 03 10 00 02 22 (ack)

# Set TPDO_1 fourth mapping (0x1A00,4) to 0x1001,0 (Error register, 8-bits)

<0x601> [8] 22 00 1A 04 08 00 01 10 (set)

<0x581> [8] 60 00 1A 04 08 00 A1 60 (ack)

# Set TPDO_1 mapping count (0x1A00,0) to 4

<0x601> [5] 22 00 1A 00 04 (set)

<0x581> [8] 60 00 1A 00 04 00 00 00 (ack)

# Save object dictionary changes to EEPROM (write “SAVE” to 0x1010,1)

<0x601> [8] 22 10 10 01 73 61 76 65 (set)

<0x581> [8] 60 10 10 01 01 00 00 00 (ack, reading this object returns 1 = manual write support)

Test:

<0x080> [0] (Send SYNC)

<0x181> [7] 00 00 89 18 83 2b 00 (PDO response)

Position = 0x0000 = 0

Voltage = 0x1889 = 6281/256 = 24.5 V

Temp = 0x2B83 = 11139/256 = 43.5 C

Error = 0 (no error)