P3 CANopen Manual

Change History

| Revision | Date | Description | Originator |
| --- | --- | --- | --- |
| AA | 2016-01-18 | Original Issue | B. Zenowich |
| AB | 2016-01-18 | Fixed Scaled Feedback OD Index | B. Zenowich |
| AC | 2016-01-19 | Added more detail to Example Operation, added change history. | B. Zenowich |
| AD | 2016-01-19 | Restored change history after accidental deletion. | B. Zenowich |
| AE | 2016-02-10 | Added documentation for the “set mode” entry in the OD (index = 0x6060). | C. Woodall |
| AF | 2016-02-24 | Added documentation for the “Error” entry in the OD (index = 0x1001) Added example of how to check for an over-temperature fault. | C. Woodall |
| AG | 2016-03-01 | Added information on CANOpen OD entry 0x3F00 for accessing BarrettCAN properties Added examples for using property 0x3F00 | C. Woodall |
| AH | 2016-04-13 | Added Appendix B on supporting multi-field TPDOs | C. Woodall |
| AI | 2016-04-22 | Added safe position information. | C. Woodall |
| AJ | 2016-05-31 | Added Trapezoidal Trajectory Mode. Added over current error to Error register. | C. Woodall |
| AK | 2016-06-21 | Updated some fields which were marked with the wrong Read-Write permissions | C. Woodall |
| AL | 2017-03-24 | Added Target Velocity, Target Position, and more documentation on the BarrettCAN Link including an example of writing to Auto-Homing and Saving the Change To EEPROM | C. Woodall |
| AM | 2017-07-19 | Added LOAD, control word, status word, quick stop option code, raw position command, raw position feedback, actual current feedback, bitfield of supported drive modes. Updated 0x6060 modes to match DSP-402 standard. Corrected velocity target units. Added a Notes section, Finite State Automaton (FSA) flow chart, and a “How it was tested” section. Reorganized Appendix B: Examples | B. Zenowich |
| AN | 2017-07-20 | Added Motor Is Homed flag (0x2402,0) | B. Zenowich |
| AO | 2017-09-21 | Added new Velocity, CSV, CSP modes. Added Faults/Warnings/EMCY codes. | B. Zenowich |
| AP | 2017-09-22 | Corrected Control Mode data type | B. Zenowich |
| AQ | 2017-09-27 | Added SYNC loss fault timeout | B. Zenowich |

Supports:

- Network Management (NMT) messages

- Heartbeat producer

- Expedited Service Data Object (SDO) messages

- Byte-level Receive/Transmit Process Data Objects (RPDOs/TPDOs)

- Sync messages for RPDOs/TPDOs

- Up to 4 RPDOs and 4 TPDOs

- Up to 4 mappable objects per PDO

- Dynamic RPDO/TPDO configuration

- SDO abort message generation

- Optional “Boot to Operational State” (0x1F80)

- Single pair of static SDO Connection Object Identifiers (COB IDs), 0x600/0x580 + NodeID

- 11-bit CAN 2.0A identifiers

- Control word (0x6040), except halt

- Status word (0x6041), except remote, target reached

- Drive modes: Idle (0), Velocity (2), Cyclic Sync Velocity (9), Cyclic Sync Position (8)

- Emergency messages

- Error registers (0x1001, 0x1002, 0x1003, 0x603F)

- Object Dictionary “dummy” entries

Does not yet support:

- Heartbeat consumption

- Timestamps

- Segmented SDOs

- Block transfer SDOs

- SDO size indication (all Tx SDOs are 8 bytes regardless of payload type)

- Bit-level RPDOs/TPDOs

- Remote Transmit Request (RTR) messages

- Multiple/dynamic SDO COB IDs

- NMT master discovery

- TPDO inhibit timers

- TPDO event timers

- 29-bit CAN 2.0B identifiers

- Deceleration ramps when switching from Operation Enabled

Boot Sequence (from the device’s perspective)

- Initialize DSP

- Initialize CANopen subsystem

- Transmit boot-up message

- Enter specified state

- Transmit heartbeat messages, if configured

Operational States

- Boot-up

  - Does not consume any messages

  - Only able to produce the boot-up message

  - Automatically enters Pre-op state after initialization and boot-up transmission

- Stopped

  - Communication limited to NMT and heartbeats only

- Pre-operational

  - All messages except PDOs are allowed

  - Send responses to SYNC messages

- Operational

  - All messages are allowed

- Reset Node

  - Performs a power-on reset (full reset)

- Reset Communication

  - Resets the CAN device then enters Boot-up state

Object Dictionary Key:

| Term | Definition |
| --- | --- |
| U08 | Unsigned 8-bit integer |
| U16 | Unsigned 16-bit integer |
| U32 | Unsigned 32-bit integer |
| I08 | Signed 8-bit integer |
| I16 | Signed 16-bit integer |
| I32 | Signed 32-bit integer |
| RO | Read-Only |
| RW | Read-Write |

DS-301 Communication

| Index | SubIdx | Type | Access | Description |
| --- | --- | --- | --- | --- |
| 0x1000 | 0 | U32 | RO | Device Type low16=profile, high16=addt'l info |
| 0x1001 | 0 | U08 | RO | Error bitfield (see below) |
| 0x1002 | 0 | U32 | RO | Manufacturer Status Register |
| 0x1003 | 0 | U08 | RO | Error history, record count |
| 0x1003 | 1-8 | U32 | RO | Error history, most recent error is at 0x1003,1 |
| 0x1005 | 0 | U32 | RW | Sync COB ID |
| 0x1006 | 0 | U32 | RO | Sync period in microseconds (iff producer) |
| 0x1008 | 0 | STR | RO | Mfg device name (4 chars) |
| 0x1009 | 0 | STR | RO | Mfg hardware version (4 chars) |
| 0x1010 | 0 | U08 | RO | Save, number of entries = 1 |
| 0x1010 | 1 | U32 | RW | Save All (write 0x65766173 “SAVE”) |
| 0x100A | 0 | STR | RO | Mfg software version (4 chars) |
| 0x1014 | 0 | U32 | RW | Emergency COB ID (default = 0x80 + NodeID) |
| 0x1015 | 0 | U16 | RW | Emergency inhibit time |
| 0x1017 | 0 | U16 | RW | Heartbeat period in milliseconds |
| 0x1018 | 0 | U08 | RO | Identity, number of entries = 6 |
| 0x1018 | 1 | U32 | RO | Vendor ID |
| 0x1018 | 2 | U32 | RO | Product code |
| 0x1018 | 3 | U32 | RO | Revision number |
| 0x1018 | 4 | U32 | RO | Serial number |
| 0x1018 | 5 | U32 | RW | Machine code |
| 0x1018 | 6 | U32 | RW | Role code |
| 0x1200 | 0 | U08 | RO | SDO parameters, number of entries = 2 |
| 0x1200 | 1 | U32 | RO | SDO receive COB ID, default = 0x600 + NodeID |
| 0x1200 | 2 | U32 | RO | SDO transmit COB ID, default = 0x580 + NodeID |
| 0x1400-0x1403 | 0 | U08 | RO | RPDO parameters, number of entries = 2 |
| 0x1400-0x1403 | 1 | U32 | RW | RPDO COB ID |
| 0x1400-0x1403 | 2 | U08 | RW | RPDO Rx type: 0-240 = Apply on nth Sync, 254 = Mfg specific, 255 = Async (Apply upon receipt) |
| 0x1600-0x1603 | 0 | U08 | RW | RPDO mapping, number of mapped objects (0-4) |
| 0x1600-0x1603 | 1-4 | U32 | RW | RPDO mapping, bits 16-31: Index, bits 8-15: SubIdx, bits 0-7 bit length (8, 16, or 32 bits) |
| 0x1800-0x1803 | 0 | U08 | RO | TPDO parameters, number of entries = 5 |
| 0x1800-0x1803 | 1 | U32 | RW | TPDO COB ID |
| 0x1800-0x1803 | 2 | U08 | RW | TPDO Tx type: 0-240 = Tx on nth Sync, 254 = Mfg specific, 255 = Async |
| 0x1800-0x1803 | 3 | U16 | RW | TPDO inhibit time in multiples of 100 uS (not implemented) |
| 0x1800-0x1803 | 4 | U08 | RO | Unused |
| 0x1800-0x1803 | 5 | U16 | RW | TPDO event timer in ms |
| 0x1A00-0x1A03 | 0 | U08 | RW | TPDO mapping, number of mapped objects (0-4) |
| 0x1A00-0x1A03 | 1-4 | U32 | RW | TPDO mapping, bits 16-31: Index, bits 8-15: SubIdx, bits 0-7 bit length (8, 16, or 32 bits) |
| 0x1F80 | 0 | U32 | RW | NMT startup (0 = Boot to Operational, 4 = Boot to Pre-op) |

States and Modes

| Index | SubIdx | Type | Access | Description |
| --- | --- | --- | --- | --- |
| 0x6040 | 0 | U16 | RW | Control Word |
| 0x6041 | 0 | U16 | RO | Status Word |
| 0x605A | 0 | U16 | RW | Quick stop option code. If value = [5, 6, 7, 8] when Quick Stop is commanded, remain in Quick Stop State (enabled, holding position), else transition to Switch On Disabled state. |
| 0x6060 | 0 | U08 | RW | Set mode of operation (0 = Idle, 1 = Profile Position, 6 = Homing, 8 = Cyclic Position, 9 = Cyclic Velocity, 10 = Cyclic Torque) |
| 0x6061 | 0 | U08 | RO | Read mode of operation |
| 0x6502 | 0 | U32 | RO | Bitfield of supported drive modes |

General feedback

| Index | SubIdx | Type | Access | Description |
| --- | --- | --- | --- | --- |
| 0x2201 | 0 | I16 | RO | Bus voltage returned as a Q8.8 signed integer. |
| 0x2202 | 0 | I16 | RO | Ambient temperature returned as a Q8.8 signed integer. |
| 0x6044 | 0 | I32 | RO | Velocity sensor value (cts/sec) |
| 0x6064 | 0 | I32 | RW | Raw position (cts), writeable in IDLE mode only |
| 0x6078 | 0 | I16 | RO | Actual current feedback, -1000 to +1000 of rated current |
| 0x603F | 0 | U16 | RO | Last error (EMCY code), also copied to 0x1003 history |

Velocity parameters (control/feedback)

| Index | SubIdx | Type | Access | Description |
| --- | --- | --- | --- | --- |
| 0x6042 | 0 | I32 | RW | Target Velocity, Immediate (Mode 2) (cts/sec) |
| 0x60FF | 0 | I32 | RW | Target velocity, Cyclic Sync (Mode 9) (cts/sec) |
| 0x6043 | 0 | I32 | RO | Target velocity after min/max limit and accel/decel ramp limit (cts/sec) |
| 0x6044 | 0 | I32 | RO | Velocity sensor value (cts/sec) |

Velocity parameters (configuration)

| Index | SubIdx | Type | Access | Description |
| --- | --- | --- | --- | --- |
| 0x6046 | 0 | U08 | RO | Velocity Limits |
| 0x6046 | 1 | U32 | RW | Minimum Velocity (cts/sec) |
| 0x6046 | 2 | U32 | RW | Maximum Velocity (cts/sec) |
| 0x6048 | 0 | U08 | RO | Acceleration record |
| 0x6048 | 1 | U32 | RW | Acceleration delta-velocity (dv) (cts/sec) |
| 0x6048 | 2 | U16 | RW | Acceleration delta-time (dt) (sec) |
| 0x6049 | 0 | U08 | RO | Deceleration record |
| 0x6049 | 1 | U32 | RW | Deceleration delta-velocity (dv) (cts/sec) |
| 0x6049 | 2 | U16 | RW | Deceleration delta-time (dt) (sec) |
| 0x60C2 | 0 | U08 | RO | Interpolation time period record |
| 0x60C2 | 1 | U08 | RW | Interpolation time period value |
| 0x60C2 | 2 | I08 | RW | Interpolation time period scale (10^n), use -3 for ms |
| 0x2381 | 0 | U08 | RO | Velocity loop gains record |
| 0x2381 | 1 | U16 | RW | Velocity proportional gain numerator |
| 0x2381 | 2 | U16 | RW | Velocity integral gain numerator |
| 0x2381 | 3 | U16 | RW | Velocity proportional gain denominator (2^n) |
| 0x2381 | 4 | U16 | RW | Velocity integral gain denominator (2^n) |
| 0x2106 | 0 | U16 | RW | Velocity loop output filter (Hz), set to zero to bypass |
| 0x2108 | 0 | U16 | RW | Velocity loop input filter (Hz), applied to vel demand and vel feedback, set to zero to bypass |

Position parameters (control/feedback)

| Index | SubIdx | Type | Access | Description |
| --- | --- | --- | --- | --- |
| 0x607A | 0 | I32 | RW | Target Position, Cyclic Sync (Mode 8) (cts) |
| 0x60B0 | 0 | I32 | RW | Position Offset (cts), default = 0 |
| 0x60B1 | 0 | I32 | RW | Velocity offset (cts/sec), default = 0 |
| 0x6064 | 0 | I32 | RW | Raw position (cts), writeable in IDLE mode only |
| 0x60F4 | 0 | I32 | RO | Position following error (cts) |
| 0x60FC | 0 | I32 | RO | Target position after min/max limit (cts) |

Position parameters (configuration)

| Index | SubIdx | Type | Access | Description |
| --- | --- | --- | --- | --- |
| 0x607D | 0 | U08 | RO | Position Limit Record |
| 0x607D | 1 | I32 | RW | Position minimum (cts) |
| 0x607D | 2 | I32 | RW | Position maximum (cts) |
| 0x6065 | 0 | U32 | RW | Position tracking warning window (cts) |
| 0x6066 | 0 | U16 | RW | Position tracking warning timeout (ms) |
| 0x2120 | 0 | U32 | RW | Position tracking fault window (cts) |
| 0x2121 | 0 | U16 | RW | Position tracking fault timeout (ms) |
| 0x60C2 | 0 | U08 | RO | Interpolation time period record |
| 0x60C2 | 1 | U08 | RW | Interpolation time period value |
| 0x60C2 | 2 | I08 | RW | Interpolation time period scale (10^n), use -3 for ms |
| 0x2382 | 0 | U08 | RO | Position loop gains record |
| 0x2382 | 1 | U16 | RW | Position proportional gain numerator |
| 0x2382 | 2 | U16 | RW | Position integral gain numerator |
| 0x2382 | 3 | U16 | RW | Position proportional gain denominator (2^n) |
| 0x2382 | 4 | U16 | RW | Position integral gain denominator (2^n) |

* Output of the position interpolation is sent to the PI position controller

* Output of the position controller is a velocity sent to 0x6042, then the Velocity mode (2) takes over.

Faults and Warnings

| Error Description | EMCY Code | OD Warn | OD Fault | Type | Units | 0x1001 bit | 0x1002 bit | States |  | Notes |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Watchdog reset | 0x6010 |  | x | U08 | Boolean | 0 | 0 | All |  | Emitted after boot-up message if reset was due to watchdog |
| Parameter error | 0x6320 |  | x | U08 | Boolean | 0 | 1 | All |  | Checks for out-of-range and valid configuration hash |
| Encoder feedback error | 0x7320 |  | x | U08 | Boolean | 0 | 2 | All |  | Invalid encoder feedback. Set to 1 to generate EMCY message & fault when error occurs. |
| Encoder magnet distance | 0x7321 |  | 0x2403,0 | U08 | Boolean | 0 | 3 | All |  | Set to 1 to generate EMCY message & fault when error occurs |
| Current limit active | 0x2310 | 0x2111,0 |  | U16 | 0.01 A | 1 | 4 | OpEn |  | User Continuous Current. Also requires 0x2110,0 U16 User Peak Current (0.01 A) and 0x2112,0 U16 User Peak Current Time (ms) |
| Short-circuit detected | 0x2320 |  | x | U08 | Boolean | 1 | 5 | OpEn |  | Peak Current exceeded. Set to 1 to generate EMCY message & fault when error occurs. |
| Bus over voltage | 0x3210 |  | 0x2384,6 | U16 | 0.1 V | 2 | 6 | All |  | Amplifier Max Voltage |
| Bus under voltage | 0x3220 |  | 0x2384,7 | U16 | 0.1 V | 2 | 7 | All |  | Amplifier Min Voltage |
| Amplifier over temperature | 0x4210 |  | 0x2384,9 | U08 | Dec C | 3 | 8 | OpEn |  | Amplifier Max Temperature |
| Motor over temperature | 0x4310 |  | 0x220A,0 | U08 | Deg C | 3 | 9 | OpEn |  | Motor Max Temperature |
| CAN overrun (frames lost) | 0x8110 |  | 0x2404,0 | U08 | Boolean | 4 | 10 | All |  | Set to 1 to generate EMCY message & fault |
| SYNC loss fault timeout | 0x8180 |  | 0x2406,0 | U16 | ms | 4 | 11 | All |  | The drive will fault if it does not hear periodic SYNCs |
| Recovered from bus-off | 0x8140 |  | 0x2405,0 | U08 | Boolean | 4 | 12 | All |  | Set to 1 to generate EMCY message & fault |
| Motor phasing error | 0x7122 |  | x | U08 | Boolean | 7 | 13 | OpEn |  | Set to 1 to generate EMCY message & fault |
| Positive limit switch | 0x7380 |  | x | U08 | Boolean | 7 | 14 | OpEn |  | Set to 1 to generate EMCY message & fault. Ignored in Idle/Homing modes. |
| Negative limit switch | 0x7381 |  | x | U08 | Boolean | 7 | 15 | OpEn |  | Set to 1 to generate EMCY message & fault. Ignored in Idle/Homing modes. |
| Homing switch | 0x7382 |  | x | U08 | Boolean | 7 | 16 | OpEn |  | Set to 1 to generate EMCY message & fault. Ignored in Idle/Homing modes. |
| Positive soft stop | 0x7383 | x |  | U08 | Boolean | 7 | 17 | OpEn |  | Set to 1 to generate EMCY message |
| Negative soft stop | 0x7384 | x |  | U08 | Boolean | 7 | 18 | OpEn |  | Set to 1 to generate EMCY message |
| Position wrapped | 0x73A0 |  | x | U08 | Boolean | 7 | 19 | All |  | Set to 1 to generate EMCY message & fault |
| Velocity tracking warning | 0x8411 | 0x606D,0 |  | U16 | cts/sec | 7 | 20 | OpEn |  | Velocity Tracking Warning Window. Also requires 0x606E,0 U16 Velocity Tracking Warning Timeout (ms) |
| Velocity tracking fault | 0x8414 |  | 0x2104,0 | U16 | cts/sec | 7 | 21 | OpEn |  | Velocity Tracking Fault Window. Also requires 0x2105,0 U16 Velocity Tracking Fault Timeout (ms) |
| Velocity limit active | 0x8418 | 0x6046,1 |  | U32 | cts/sec | 7 | 22 | OpEn |  | Max Velocity Limit. Use 0x6046,2 U32 for Min Velocity Limit (same EMCY message) |
| Acceleration limit active | 0x8480 | 0x60C5,0 |  | U32 | cts/sec/sec | 7 | 23 | OpEn |  | Acceleration Limit. Use 0x60C6,0 U32 for Deceleration Limit (same EMCY message) |
| Position tracking warning | 0x8611 | 0x6065,0 |  | U32 | cts | 7 | 24 | OpEn |  | Position Tracking Warning Window. Also requires 0x6066,0 U16 Position Tracking Warning Timeout (ms) |
| Homing error | 0x8613 |  | x | U08 | Boolean | 7 | 25 | OpEn |  | Failed to achieve minimum homing range. Set to 1 to generate EMCY message & fault when error occurs. |
| Position tracking fault | 0x8614 |  | 0x2120,0 | U32 | cts | 7 | 26 | OpEn |  | Position Tracking Fault Window. Also requires 0x2121,0 U16 Position Tracking Fault Timeout (ms) |

Notes:

Only the BOLD errors have been implemented.

Warnings are auto-reset when the condition clears.

Faults are latched, amplifier transitions to fault state, motor voltage is disabled.

Transitioning from Fault to Switch On Disabled clears all latched faults, but if the fault condition still exists, it will re-trigger the fault.

EMCY message format: MsgID=0x80|NodeID, DLC=8, [CodeLow, CodeHigh, 0x1001, 0, 0, 0, ResetCodeLow, ResetCodeHigh].

The last emitted (non-zero) EMCY code is stored in 0x603F,0 U16 and 0x1003,1 U32 (lower 16 bits), and its corresponding bit is set in 0x1002.

When an error condition is cleared, an EMCY message is emitted with code = 0x0000, an updated 0x1001, and the code of the corresponding cleared error.

To disable a warning/fault, set its value to zero.

BarrettCAN Property Access

| Index | SubIdx | Type | Access | Description |
| --- | --- | --- | --- | --- |
| 0x3F00 | 0-127 | U16 or U32 | RW | BarrettCAN Property Access. The sub-index maps to the BarrettCan Property. So sub-index 20 (0x14) will read the THERM property and sub-index 50 (0x32) will read the DP parameter. See the P3_RSF-5B document for a complete list of BarrettCAN properties. The length of these parameters is related to the length of the parameters in BarrettCAN. A majority of parameters are 16 bits, but some are 32bits. All bytes are sent little-endian. |
| 0x3F00 | 30 | U16 | RW | SAVE a BarrettCAN property from RAM to EEPROM. Send the BarrettCAN property ID to save. For example, to save MDS, set 0x3F00,30 to 65 (as a 16 bit unsigned integer). |
| 0x3F00 | 31 | U16 | RW | LOAD a BarrettCAN property from EEPROM to RAM. Send the BarrettCAN property ID to load. For example, to load MDS, set 0x3F00,31 to 65 (as a 16 bit unsigned integer). |
| 0x3F00 | 65 | U16 | RW | BarrettCAN property MDS (Auto-Homing Delay Time in milliseconds). Set to 0 to disable auto homing. |

Miscellaneous

| Index | SubIdx | Type | Access | Description |
| --- | --- | --- | --- | --- |
| 0x2401 | 0 | U16 | RW | 16-bit Unsigned Scaled Safe Position. |
| 0x2402 | 0 | U08 | RO | Motor Is Homed flag |
| 0x6062 | 0 | I32 | RW | Raw position demand |
| 0x60A0 | 0 | U16 | RW | Scaled position command |
| 0x60A1 | 0 | U16 | RO | Scaled position feedback |

Error bitfield (0x1001,0):

| Bit | Meaning |
| --- | --- |
| 0 | Generic error. Plus, if any higher bit is set, this bit is also set. |
| 1 | Motor current error |
| 2 | Motor voltage error |
| 3 | Temperature error |
| 4 | Communication error |
| 5 | Unused |
| 6 | Unused |
| 7 | Motion control error |

Notes:

P3 does not yet support deceleration ramps when transitioning out of Operation Enabled state.

The Control Mode Display (0x6061) is cleared to zero upon entering the state Operation Enabled.

The Control Mode (0x6060) can only be set to a non-zero value when the state is Operation Enabled.

Writing to the scaled position demand (0x60A0) only works if:

- The motor is homed

- The state is Operation Enabled

- The control mode display (0x6061) is either 1 (position profile) or 8 (cyclic sync position)

Writing to the raw position demand (0x6062) only works if:

- The state is Operation Enabled

- The control mode display (0x6061) is either 1 (position profile) or 8 (cyclic sync position)

Writing to the raw position (0x6064) only works if the Control Mode Display (0x6061) is 0 (Idle).

The status word 0x6041 is mappable to a PDO and contains bits (13,12,10) indicating the homing status while the Control Mode Display (0x6061) is Homing (6).

- 000 = homing

- 001 = interrupted

- 011 = success

Changing the control mode clears the mode-specific status bits.

Autohoming breaks several CANopen rules. The state machine, status, and control mode do not reflect the actual state while autohoming. Until we can decide on a solution, I don’t recommend enabling Autohoming if you want to use CANopen.

Normal homing and homing interruption work as expected over CANopen. The process still references the BarrettCAN GUI homing parameters. There is no “Home Immediate” homing method implemented yet.

Actual current feedback is functional, but I’m not 100% confident in the units yet. It could be off by a factor of 2 or more.

How it was tested:

After power on, send NMT Pre-op (80 00) or NMT Go Op (01 00).

You will start to get Heartbeats.

Send Ready to Switch On

Send Operation Enabled

Set Mode to Homing

Send Switched On (interrupts homing)

Send Operation Enabled

Set Mode to Homing (restarts homing)

Get Status Word, check bits 13,12,10 for homing status

(wait for homing to complete)

Set Mode to Cyclic Pos

Write Scaled Dmd Pos = 0x0000 (motor moves)

Write Scaled Dmd Pos = 0xF000 (motor moves)

Set Mode to Idle

Get Raw Position (returns some big number)

Set Raw Position to zero

Get Raw Position (returns a value near zero)

Set Mode to Profile Pos

Write Dmd Pos = 0xF000 (motor moves)

Write Dmd Pos = 0x0000 (motor moves)

Motor is now holding position, so Get Actual Current repeatedly while trying to deflect the motor shaft, watch current value rise/fall.

CANopen Finite State Automaton (FSA)

Appendix A – CANopen Message Format

- Network Management (NMT)

  - MsgID = 0x000 (heard by all nodes)

  - DLC = 2

  - Payload = [Commanded_State] [NodeID]

    - Commanded_State

      - 0x01 = Operational

      - 0x02 = Stopped

      - 0x80 = Pre-operational

      - 0x81 = Reset Node

      - 0x82 = Reset Communications

    - NodeID

      - 0 = All nodes

      - >0 = Single node

- Heartbeat

  - MsgID = 0x700 | NodeID

  - DLC = 1

  - Payload = [State]

    - State

      - 0x00 = Boot-up

      - 0x04 = Stopped

      - 0x05 = Operational

      - 0x7F = Pre-operational

- SYNC

  - MsgID = 0x080

  - DLC  = 0

- Emergency

  - MsgID = 0x080 | NodeID

  - DLC = 8

  - Payload = [ErrLow] [ErrHigh] [ErrRegister] [Mfg-Specific]…

    - [ErrLow] [ErrHigh] = 16-bit CANopen error code

    - [ErrRegister] = copy of OD 1001,00

    - [Mfg-Specific] = 0-5 bytes of error data (optional)

- Timestamp

  - MsgID = 0x100

  - DLC = 4

  - Payload = 32-bit timestamp value (LSB)

- SDO Write (Expedited) – Write this data to the Object Dictionary (OD)

  - MsgID = 0x600 | NodeID

  - DLC = 8

  - Payload = [0010 nn e s] [lowIdx] [highIdx] [subIdx] [ data ]…

    - 0010 = SDO Write

    - nn = number of bytes w/o data (iff s == 1)

    - e = Expedited

    - s = size indicated in nn

    - [lowIdx] [highIdx] = 16-bit OD index

    - [subIdx] = OD entry sub-index

    - [data] = 1-4 bytes of data (little-endian)

- SDO Write Ack – Data was written to the OD

  - MsgID = 0x580 | NodeID

  - DLC = 8

  - Payload = [0110 0000] [lowIdx] [highIdx] [subIdx] 0x00 0x00 0x00 0x00

- SDO Read – Read data from OD

  - MsgID = 0x600 | NodeID

  - DLC = 8

  - Payload = [0100 0000] [lowIdx] [highIdx] [subIdx] 0x00 0x00 0x00 0x00

- SDO Read Response (Expedited) – Here is the data you requested

  - MsgID = 0x580 | NodeID

  - DLC = 8

  - Payload = [0100 nn e s] [lowIdx] [highIdx] [subIdx] [ data ]…

    - 0100 = SDO Read

    - nn = number of bytes w/o data (iff s == 1)

    - e = Expedited

    - s = size indicated in nn

    - [lowIdx] [highIdx] = 16-bit OD index

    - [subIdx] = OD entry sub-index

    - [data] = 1-4 bytes of data (little-endian)

- Receive PDO – process data object to be received by the device

  - MsgID = 0x200 | NodeID, 0x300 | NodeID, etc.

  - DLC = n (byte count)

  - Payload = [data]…

    - [data] = little-endian data

- Transmit PDO – process data object to be transmitted by the device

  - MsgID = 0x180 | NodeID, 0x280 | NodeID, etc.

  - DLC = n (byte count)

  - Payload = [data]…

    - [data] = little-endian data

Appendix B – Examples

Example configuration for Node 1:

<MessageID> [Data Length Code] byte0 byte1… (all in hexadecimal)

# Go Pre-op (received PDOs not processed in Pre-op)

<0x000> [2] 80 01 (NMT)

<0x701> [1] 7f (heartbeat)

# Set Sync COB ID to 0x080

<0x601> [8] 22 05 10 00 80 00 00 00 (set)

<0x581> [8] 60 05 10 00 80 00 00 00 (ack)

# Set Heartbeat MS to 0x03E8 = 1000 ms

<0x601> [6] 22 17 10 00 E8 03 (set)

<0x581> [8] 60 17 10 00 E8 03 00 00 (ack)

# Set RPDO_1 COB ID (0x1400,1) to 0x201

<0x601> [8] 22 00 14 01 01 02 00 00 (set)

<0x581> [8] 60 00 14 01 01 02 00 00 (ack)

# Set RPDO_1 Rx type (0x1400,2) to 0xFF (async, process immediately,

# do not wait for SYNC)

<0x601> [5] 22 00 14 02 FF (set)

<0x581> [8] 60 00 14 02 FF 00 00 00 (ack)

# Set RPDO_1 first mapping (0x1600,1) to 0x60A0,0 (Scaled position cmd,

# 16-bits)

<0x601> [8] 22 00 16 01 10 00 A0 60 (set)

<0x581> [8] 60 00 16 01 10 00 A0 60 (ack)

# Set RPDO_1 mapping count (0x1600,0) to 1

<0x601> [5] 22 00 16 00 01 (set)

<0x581> [8] 60 00 16 00 01 00 00 00 (ack)

# Set TPDO_1 COB ID (0x1800,1) to 0x181

<0x601> [8] 22 00 18 01 81 01 00 00 (set)

<0x581> [8] 60 00 18 01 81 01 00 00 (ack)

# Set TPDO_1 Tx type (0x1800,2) to 0 (Tx on every SYNC)

<0x601> [5] 22 00 18 02 00 (set)

<0x581> [8] 60 00 18 02 00 00 00 00 (ack)

# Set TPDO_1 Inhibit time (0x1800,3) to 0 (unused)

<0x601> [6] 22 00 18 03 00 00 (set)

<0x581> [8] 60 00 18 03 00 00 00 00 (ack)

# Set TPDO_1 Event timer (0x1800,5) to 0 (unused)

<0x601> [6] 22 00 18 05 00 00 (set)

<0x581> [8] 60 00 18 05 00 00 00 00 (ack)

# Set TPDO_1 first mapping (0x1A00,1) to 0x60A1,0 (Scaled position feedback,

# 16-bits)

<0x601> [8] 22 00 1A 01 10 00 A1 60 (set)

<0x581> [8] 60 00 1A 01 10 00 A1 60 (ack)

# Set TPDO_1 mapping count (0x1A00,0) to 1

<0x601> [5] 22 00 1A 00 01 (set)

<0x581> [8] 60 00 1A 00 01 00 00 00 (ack)

# Save object dictionary changes to EEPROM (write “SAVE” to 0x1010,1)

<0x601> [8] 22 10 10 01 73 61 76 65 (set)

<0x581> [8] 60 10 10 01 01 00 00 00 (ack, reading this object returns 1 = manual write support)

# Reboot node 1

<0x000> [2] 81 01 (NMT)

Example operation:

# Apply power

# Wait at least 5 ms for P3 to boot up

# Go Operational (switches from BarrettCAN to CANopen, RPDOs and TPDOs enabled)

<0x000> [2] 01 00 	NMT – Go Operational, all nodes

# Initial heartbeats

<0x701> [1] 05 	Puck 1 responds with its initial heartbeat

<0x702> [1] 05 	Puck 2 responds with its initial heartbeat

# First control loop iteration, RPDOs sent from master to pucks

<0x201> [2] 34 12 	Master sends Puck 1 a scaled position command = 0x1234

<0x202> [2] 56 34 	Master sends Puck 2 a scaled position command = 0x3456

# Master asks for puck TPDOs

<0x080> [0] 	Master sends a Sync to get position feedback from all nodes

# Pucks respond with their TPDOs

<0x181> [2] 20 12 	Puck 1 responds with its scaled position feedback = 0x1220

<0x182> [2] 50 34 	Puck 2 responds with its scaled position feedback = 0x3450

# Second control loop iteration…

<0x201> [2] 56 12 	Master sends Puck 1 a scaled position command = 0x1256

<0x202> [2] 89 34 	Master sends Puck 2 a scaled position command = 0x3489

<0x080> [0] 	Master sends a Sync to get position feedback from all nodes

<0x181> [2] 33 12 	Puck 1 responds with its scaled position feedback = 0x1233

<0x182> [2] 85 34 	Puck 2 responds with its scaled position feedback = 0x3485

# … N iterations

Example: Reading errors

Example: Reading BarrettCAN parameters:

# In The GO-OP State

# Get the Default Position (DP) property 50.

<0x601> [4] 40 00 3F 32

<0x581> [8] 42 00 3F 32 00 80 00 00

# Get the Thermistor Temperature (THERM) property 20.

<0x601> [4] 40 00 3F 14

<0x581> [8] 42 00 3F 32 00 1E 00 00

CANopen Multi-Field TPDO

# Set TPDO_1 COB ID (0x1800,1) to 0x181

<0x601> [8] 22 00 18 01 81 01 00 00 (set)

<0x581> [8] 60 00 18 01 81 01 00 00 (ack)

# Set TPDO_1 Tx type (0x1800,2) to 0 (Tx on every SYNC)

<0x601> [5] 22 00 18 02 00 (set)

<0x581> [8] 60 00 18 02 00 00 00 00 (ack)

# Set TPDO_1 Inhibit time (0x1800,3) to 0 (unused)

<0x601> [6] 22 00 18 03 00 00 (set)

<0x581> [8] 60 00 18 03 00 00 00 00 (ack)

# Set TPDO_1 Event timer (0x1800,5) to 0 (unused)

<0x601> [6] 22 00 18 05 00 00 (set)

<0x581> [8] 60 00 18 05 00 00 00 00 (ack)

# Set TPDO_1 first mapping (0x1A00,1) to 0x60A1,0 (Scaled position feedback, 16-bits)

<0x601> [8] 22 00 1A 01 10 00 A1 60 (set)

<0x581> [8] 60 00 1A 01 10 00 A1 60 (ack)

# Set TPDO_1 second mapping (0x1A00,2) to 0x2201,0 (Bus voltage, 16-bits)

<0x601> [8] 22 00 1A 02 10 00 01 22 (set)

<0x581> [8] 60 00 1A 02 10 00 01 22 (ack)

# Set TPDO_1 third mapping (0x1A00,3) to 0x2202,0 (Amplifier temperature, 16-bits)

<0x601> [8] 22 00 1A 03 10 00 02 22 (set)

<0x581> [8] 60 00 1A 03 10 00 02 22 (ack)

# Set TPDO_1 fourth mapping (0x1A00,4) to 0x1001,0 (Error register, 8-bits)

<0x601> [8] 22 00 1A 04 08 00 01 10 (set)

<0x581> [8] 60 00 1A 04 08 00 A1 60 (ack)

# Set TPDO_1 mapping count (0x1A00,0) to 4

<0x601> [5] 22 00 1A 00 04 (set)

<0x581> [8] 60 00 1A 00 04 00 00 00 (ack)

# Save object dictionary changes to EEPROM (write “SAVE” to 0x1010,1)

<0x601> [8] 22 10 10 01 73 61 76 65 (set)

<0x581> [8] 60 10 10 01 01 00 00 00 (ack, reading this object returns 1 = manual write support)

Test of CANopen Multi-Field TPDO:

<0x080> [0] (Send SYNC)

<0x181> [7] 00 00 89 18 83 2b 00 (PDO response)

Position = 0x0000 = 0

Voltage = 0x1889 = 6281/256 = 24.5 V

Temp = 0x2B83 = 11139/256 = 43.5 C

Error = 0 (no error)

Example of Disabling Auto-Homing, Saving to EEPROM, and Sending Velocity.

# Send NMT message to Go Operational

<0x000> [2] 01 00

# Heartbeat Response From Node 31

<0x71F> [1] 7F

# Set BarrettCAN Link (0x3F00) Property 65 (Auto-Homing Timeout) to 0 to disable Autohoming

<0x61F> [6] 22 00 3F 41 00 00 (set)

<0x59F> [8] 60 00 3F 41 00 00 00 00 (ack)

# Read BarrettCAN Link (0x3F00) Property 65 (Auto-Homing Timeout)

<0x61F> [6] 40 00 3F 41 00 00 (set)

<0x59F> [8] 42 00 3F 41 00 00 00 00 (ack)

# Set BarrettCAN Link (0x3F00) Property 30 to 65 to Save property 65 (Auto-Homing Timeout) to EEPROM

<0x61F> [6] 22 00 3F 1E 41 00 (set)

<0x59F> [8] 60 00 3F 1E 00 00 00 00 (ack)

# Set MODE (0x6060,00) to VELOCITY (3)

<0x61F> [8] 22 60 60 00 03 00 00 00

<0x59F> [8] 60 60 60 00 03 00 00 00

# Set Target Velocity (0x60FF,0) to 32.0625 Radians (0x101010/(2^16))

<0x61F> [8] 22 FF 60 00 10 10 10 00

<0x59F> [8] 60 FF 60 00 00 10 20 00